## Slide 1
Realization & Testing
After construction, the system was characterized in full via looped charge and discharge between PSEC’s microgrid and the 2011 Chevrolet Volt.
Operator Interface
The user interface was developed in Eaton’s Visual Designer software in order to provide a convenient way to control the system and analyze grid power flow during professional system demonstrations.
System Schematic Breakdown
Design Space
A 2011 Chevrolet Volt (hybrid) was provided by Eaton to interface with PSEC’s microgrid, a utility-tied network of generation sources and consumption loads built for system-level power flow analysis.
Electric Vehicle to Grid: Microgrid Integration
Charge Path
Discharge Path
Controls and Network
Auxiliary Circuitry
Industry Impact
With an ever-aging infrastructure, the nation’s power grid continues to face growing challenges in stability and efficiency. This problem is
Acknowledgements
We are extremely grateful to Eaton for funding the project and would like to extend personal thanks to Erik Hurd, Amit Gholam, Santino Graziani, Brandon Grainger, and Dan Carnovale for their exceptional guidance, support, and enthusiasm.
Future Plans
The system will become a permanent installation at PSEC (Warrendale, PA) for demonstration. Continual improvement is planned to implement true bidirectional charging, compacting, and integration with PSEC’s system-level microgrid controller.
Accuracy (Error%)
a. Charge to target: < 1%
b. Discharge to target: < 1%
c. Metered Data: < 1%
d. Estimated time: < 5%
Safety: all contactors open upon communication error
Speed (Constant Rates):
a. Full charge: 6hr @ 3kW
b. Full Discharge: 1.8hr @ 10kW
c. Charge-Discharge cycle: 90s
d. Discharge-Charge cycle: 15s
exacerbated with the rise of intermittent renewable energy sources like solar and wind., which cause further ssssssssssssssss
fluctuations in the energy generation and consumption throughout the day.
------
Vehicle to Grid (V2G) is an emerging technology in the power systems field. The V2G paradigm sees electric vehicles as potential mobile energy storage units – the high capacity batteries can be charged when grid demand is low and also discharged back to the grid during periods of high demand.
This selective power flow can help balance generation and demand, thereby 1. increasing efficiency, 2. reducing system strain, and 3. decreasing the risk of failure and black outs.
Notes: Dr. Modo