## Slide 1: Use of Organic Materials for the Fabrication of Flexible Memory
Seth So

## Slide 2: Content Overview
Evolution of Flexible Electronics
Fabrication Methods
Mechanisms of Modern Devices
Photopolymers
Quantum Dot
Ionic Nanocluster
Summary & Conclusions

## Slide 3: Flexible Electronics
Flexible Electronics have been rapidly growing, nearing commercial viability
Such circuitry and integrated systems will eventually call for flexible memory
Organic bases have opened many memory mechanisms
Continual research is yielding improvements at a promising rate

## Slide 4: Fabrication Methods

## Slide 5: Fabrication Methods
Spin + Lithography
Ink Jet printing
Laser Jet printing
Roll-to-Roll methods
Photos from: R. Lawson (Ref. 1)
U. Scheischang (Ref. 2)

## Slide 6: Fabrication Methods
Spin + Lithography
Ink Jet printing
Laser Jet printing
Roll-to-Roll methods
Photo from: Phoseon Technology

## Slide 7: Fabrication Methods
Spin + Lithography
Ink Jet printing
Laser Jet printing
Roll-to-Roll methods
Photo from: O. Kravchuk (Ref. 3)

## Slide 8: Fabrication Methods
Spin + Lithography
Ink Jet printing
Laser Jet printing
Roll-to-Roll methods
Photo from: University of Minnesota, MURI

## Slide 9: Devices and Mechanisms

## Slide 10: Photopolymers
DAE-Me/P3HT = diarylethene + poly(3-hexylthiopene)
3 ns laser  ultravioletoff and greenon
3-terminal 8bit storage (256 distinct levels)
Switching ratio: α 105
70 write erase cycles
500-day nonvolatility (107s)
Flex resistant (5son/off @ 8mm)
(device)
Photos from: T. Leydecker (Ref. 4)

## Slide 11: Photopolymers
DAE/P3HT = diarylethene + poly(3-hexylthiopene)
3 ns laser  ultravioletoff and greenon
3-terminal 8bit storage (256 distinct levels)
Switching ratio: α 105
70 write-erase cycles
500-day nonvolatility (107s)
Flex resistant (5son/off @ 8mm)
(characterization)
Photos from: T. Leydecker (Ref. 4)

## Slide 12: Graphidyne
(device)
Graphidyne (GD) = 2D carbon allotrope (2D C6H6 + C≡C)
GD np.s + Al-Al2O3 np.s create differential bandgap
Crossbar array can form ReRAM WORM Memory
Switching ratio: α 102
Low operation voltage (1-3V)
3-hour nonvolatility (104s)
Photos from: Z. Jin (Ref. 5)

## Slide 13: Graphidyne
(characterization)
Graphidyne (GD) = 2D carbon allotrope (2D C6H6 + C≡C)
GD np.s + Al-Al2O3 np.s create differential bandgap
Crossbar array can form ReRAM WORM Memory
Switching ratio: α 102
Low operation voltage (1-3V)
3-hour nonvolatility (104s)
Photos from: Z. Jin (Ref. 5)

## Slide 14: Ionic Nanoclusters
(device)
PAMPSA = poly(2-Acrylamido-2-methylpropane sulfonic acid)
Protonation with Aniline leads to permanent charge complex [- SO3- - +NH3 -], immobilized via annealing @ 150oC
Full WRER Capabilities, crossbar array sub cells
Switching ratio: α 102
Low operation voltage (1-5V)
Rigid Durability: > 106 cyc.
Flex. Durability: ~ 103 cyc. @ 30o
VolatilityRigid/Flex.: 108 s / 106 s
Photos from: C. Lee (Ref. 6)

## Slide 15: Ionic Nanoclusters
(characterization)
PAMPSA = poly(2-Acrylamido-2-methylpropane sulfonic acid)
Protonation with Aniline leads to permanent charge complex [- SO3- - +NH3 -], immobilized via annealing @ 150oC
Full WRER Capabilities, crossbar array sub cells
Switching ratio: α 102
Low operation voltage (1-5V)
Rigid Durability: > 105 cyc.
Flex. Durability: ~ 103 cyc. @ 30o
VolatilityRigid/Flex.: 108 s / 106 s
Photos from: C. Lee (Ref. 6)

## Slide 16: Summary & Conclusions
Necessary Improvements: Faster switching speeds (μ and relaxation), scaling to practical level, reliable durability and volatility
Much potential for development, but significant advances needed before becoming practically viable.
 | Advantages | Disadvantages
Photopolymers | High storage density, flex resistant, non-volatile, simple structure | Power intensive, high voltage operation, slow switching speed
Graphidyne | Easily scalable and altered, fast switching speed, simple structure | Low voltage operation, low switch ratio, relatively volatile
Ionic Nanoclusters | Extremely durable, flex resistant, non-volatile, high hysteresis, simple structure | Low voltage operation, low switch ratio, slow switching speed

## Slide 17: References
Lawson, R., Robinson, A., 2016. Frontiers of Nanoscience. 11. 1-90.
Zschieschang, U., Ante, F., Yamamoto, T., et al., 2010. Advanced Materials. 22. 982-985.
Kravchuck, O., Lesyuk, R., Bobitski, Y., et al. 2018. NANO 2017. Spring Proceedings in Physics. 210. 317-339.
Leydecker, T., Herder, M., Pavlica, E., et al., 2016. Nature: Nanotechnology. 11. 769-777.
Jin, Z., Chen, Y., Zhou, Q., et al., 2017. Materials: Chemistry. 1. 1338-1341
Lee, C., Jeong, J., Kim, H., et al., 2019. Materials: Horizons. 6. 1899-1905